A preliminary assessment of the impact of long-term fire treatments on in-situ soil hydrology in the Kruger National Park

Riddell, ES1*., Khan, A1., Mauck, B1., Ngcobo, S1., Pasi, J1. Pickles, A1., Pickles1,J., Sithole1, Z., Lorentz, SA1., Govender, N2

¹School of Agriculture, Earth and Environmental Science, University of KwaZulu-Natal, Private Bag X01, Scottsville, 3209, Pietermaritzburg, South Africa

2Scientific Services, South African National Parks, Kruger National Park

*Email: riddelle@ukzn.ac.za / edriddell@gmail.com

Abstract

There has been significant attention focused on the impacts of fire frequency and season of burn on ecological processes in the Kruger National Park (KNP). Whilst there has been some examination of these fire effects on soil properties, the explicit linkages of these effects to the hydrology of soils in burnt areas has remained a gap in our understanding. During August 2010 a field scoping campaign was undertaken to assess the impacts, if any, of long term fire treatments on the hydrology of soils on the Experimental Burn Plots (EBP’s) in the KNP.

Using various hydrometric and soil physical characterisation instruments soil hydraulic conductivity and soil strength variations were determined across the extreme fire treatment on the EBPs, the annual August (high fire frequency) plots and the control (no burn) plots, in both granites and basalt of Pretoriuskop and Satara, respectively.

There were soil hydrological and structural differences to fire treatments on the basalt burn plots, but not as clear on the granite burn plots. In particular, hot frequent fires appear to reduce the variation in soil hydraulic conductivity on the annual burn plots in the basalts and lead to reduced cohesive soil strength at the surface.

Introduction

Savannas are tropical grasslands with scattered trees; they occupy about 20% of the land surface of the Earth, and 40% of Africa (Scholes & Hall, 1996). These ecosystems are dynamic in their structure, composition and function. Fire is an important driver in savanna ecosystems, where it acts both as a generalist herbivore (Bond & Keeley 2005), and as a facilitator of the coexistence of trees and grasses (Higgins et al. 2000). The spatio-temporal availability of water is also considered a key driver of savanna heterogeneity (Walter, 1971). Studies of catchment hydrological processes response to natural and induced fires have received greatest attention in various land-systems within Australia (e.g. Townsend & Douglas, 2000; Brown, 1972). Studies elsewhere include mountain catchments under exotic forestry (Scott, 1997) and fynbos (Lindley et al, 1988) in South Africa, however few studies have explicitly examined pyro-hydrological interactions and the role of various burning regimes within African savannas (Scholes & Walker, 1993).

Fire has long been used in the management of savannas, and this management has been informed and adapted by the findings of on-going research on experimental sites of selected fire regimes on fixed areas (Knapp et al. 1998; Andersen et al. 2003). The long-term fire experiment in the Kruger National Park (KNP) was established in 1954. The initial objectives being to study the effects of fire frequency and season on the vegetation of the KNP under indigenous grazing pressure (Van der Schijff, 1958). The Experimental Burn Plots (EBPs) were laid out in four of the main vegetation landscapes of the KNP described by Gertenbach (1983).

Whilst there has been some examination of fire effects on in-situ soil properties, the explicit linkages of these to the hydrology of soils in burnt areas has remained a knowledge gap. To date, a variety of soil hydrological responses have been described, for instance:  frequent burning reduced the rate of infiltration of rainwater into soil as noted in the Drakensberg (Bijker et al. 2001). This is caused by crusting of the soil thereby yielding lower electrical conductivity (EC) and increasing the water runoff and increasing soil erosion as shown particularly for the granite EBPs in KNP (Mills & Fey, 2004). Webber (1979) showed that the unburnt control EBPs near Skukuza retained greater moisture levels well into the dry season, and where burning occurred on duplex soils this made them susceptible to erosion.

Methods

The August 2010 field campaign focused on describing various in-situ soil hydraulic and strength characteristics on these plots on the two extreme fire treatments on the two dominant geologies in the KNP, namely the granites at Pretoriuskop (Lowveld Sour Bushveld, sandy soils with MAP of 737 mm) and basalts at Satara (Acacia nigrescens savanna: clay soils with MAP of 537 mm) (Biggs et al. 2003).

Since one string at both sites are deemed unrepresentative of the broader landscapes (Venter & Govender, in press), only three of the four strings at these sites were assessed, as shown in Figure 1.

FIGURE 1: The KNP Experimental Burn Plot strings assessed in this study.

A semi-systematic approach was taken in order to dismiss the inherent variability associated with different soil morphologies at landscape positions. Predetermined areas were selected according to diagnostic soil form characteristics, based on expert opinion from a soil scientist (Le Roux pers comm. 2010), which resulted in attention to sites characteristic of the Shortlands and Huttons soil forms (Soil Classification Working Group, 1991) on basalt and granite, respectively. Hydrological measurements and soil characterizations were then taken randomly within these areas.

A variety of techniques that determine the soils hydraulic conductivity within 30 cm of the soil surface were used:

- Double-ring infiltrometers: to determine soil saturated conductivities (Ksat) at the soil surface, according to the method of Lorentz et al (2003)

- Guelph permeameters: to determine soil saturated conductivities (Ksat) within the subsurface at 5, 15 and 30 cm depths. (Eijkelkamp, 2008).

- Matric disc infiltrometers: to determine soil unsaturated conductivities (Kunsat) at the soil surface, according to the method of Lorentz et al (2003)

Two replicates of each of the above were made at each EBP treatment, per landscape and results are discussed simply based on visual interrogation of the data.

The unconfined cohesive soil strength on the EBPs was assessed using:

- Dynamic Cone Penetrometer (Herrick & Jones, 2002): 1 cm diameter rod, conical extremity of 90°, 2 kg weight dropped from a height of 100 cm).

- Pocket penetrometer (Eijkelkamp, 2009).

- Pocket vane tester (Eijkelkamp, 2011).

The above were performed within a 5m radius of the hydrology measurements and typically 10 readings were taken at each of the EBP’s. The resulting data was then subject to non-parametric statistical analysis using the Mann-Whitney U-test for unmatched samples using STATEXT v1.4 (2011).

Results

The Ksat values determined at the granite EBPs soil surface, clearly illustrate higher variation across all the plots and between fire treatments (Figure.2). Unfortunately no measurements were taken on the Numbi control plot, however we see that at Shabeni the control plots, for both replicates, had significantly greater Ksat values than the annual burn plots. At Kambeni the annual and control plots had similar Ksat values, although in both replicates the values were slightly lower for the control. The Ksat values for the basalt EBPs had generally lower variation than the granite EBPs (Figure.3). With the exception of Marheya replicate 1 (0.015 cm/s-1 beyond the axis range) there appears to be no distinct difference in the Ksat between annual or control treatments on the basalt EBPs.

The results of Ksat tests at depths between 5-30 cm in Figures. 2 & 3 reveal that granite soils, have on average a greater hydraulic conductivity on the annual frequent burn plots than the control, this is most noticeable at Kambeni & Shabeni. Interestingly, it appears that there is less variation in Ksat at 5 cm within the control treatments on the granites. As expected the basalts due to their finer texture have an order of magnitude lower Ksat distribution than the granites, however there is no distinct difference in Ksat between and annual and control treatments in the soil sub-surface.

Figure. 4 shows the Kunsat values of the granite EBPs soil surface, where on average the annual plots tend to have greater Kunsat than the controls. Also there is a distinctly greater Kunsat on the annual plots at the lowest soil moisture tensions close to saturation (0.5 cm).  The opposite trend of the annual EBPs having a lower Kunsat on average than the controls is demonstrated on the basalt EBP’s (Figure.5). The outlier to the above trend on the basalt was the Marheya string, that is, the control’s had greater variation in Kunsat than the annual plots.

Drop cone penetrometer tests for granite EBPs in Figure. 6 reveal that the first ~150 joules is the threshold for maximum depth penetration across annual and control plots, thereafter there is a steady increase in depth at each energy increment. The greatest variations in soil strength properties were noted for control plots compared to annual plots on the granite soil. Whilst the basalt EBPs (Figure. 7) it is the annual EBPs again having distinctly less variation in soil strength compared to the controls. An interesting aspect of Figure. 7 is the slightly lower threshold in energy over depth which is reached at about ~130 joules before further energy results in less depth penetration.

Table 1 also presents the statistical results of the raw drop cone penetrometer data at two energy levels (2 x 2 kg weight drops, or 34 Joules/cm-2; and 10 x 2 kg weight drops, or 307 Joules/cm-2). There is no significant difference in the cohesive soil strength between control and annual plots on the granite EBPs, however the basalt EBPs do show a significantly greater mean depth of penetration at both energy levels on the annual plots. The pocket penetrometer data supports this with no significant difference on the granites, but a difference on the basalts. No significant difference is observed within the soil shear strength between annual and control treatments on both geological settings.

FIGURE 2: Field saturated hydraulic conductivity versus depth at Granite EBPs

FIGURE 3: Field saturated hydraulic conductivity versus depth at Basalt EBPs

FIGURE 4: Unsaturated hydraulic conductivity at the surface, Granite EBPs

FIGURE 5: Unsaturated hydraulic conductivity at the surface, Basalt EBPs

FIGURE 6: Drop cone penetrometer data, Granite EBPs (data are averages of 10 readings at each site)

FIGURE 7: Drop cone penetrometer data, Basalt EBPs (data are averages of 10 readings at each site)

Table 1: Mann-Whitney U- test results for unconfined cohesive soil strength parameters (with no differentiation of the EBP string within the analysis).

|  |  | Basalt | Granite |
| --- | --- | --- | --- |
|  |  | N | Mean | U | P | N | Mean | U | P |
| Pocket Penetrometer (Kg/cm-2) | Annual | 62 | 2.51 | 1295 | 0.000 | 22 | 2.05 | 233.5 | 0.100 |
|  | Control | 69 | 1.82 |  |  | 27 | 1.62 |  |  |
| Pocket Vane Tester (Kg/cm-2) | Annual | 46 | 2.63 | 814 | 0.295 | 22 | 2.27 | 262 | 0.483 |
|  | Control | 38 | 2.74 |  |  | 24 | 1.94 |  |  |
| Drop Cone Penetrometer (34 J/cm-2) | Annual | 30 | 2.18 | 283.5 | 0.006 | 30 | 1.76 | 327.5 | 0.107 |
|  | Control | 30 | 1.72 |  |  | 27 | 2.14 |  |  |
| Drop Cone Penetrometer (307 J/cm-2) | Annual | 30 | 4.67 | 332.5 | 0.041 | 30 | 4.8 | 385 | 0.458 |
|  | Control | 30 | 4.04 |  |  | 27 | 4.77 |  |  |

Discussion

These measurements reveal interesting differences across geologies and long-term fire and no fire treatments. In the absence of greater spatial and temporal replication, the interpretation at this stage is speculative, but sets the scene for future data collection and analysis.  Nevertheless key aspects and questions from these initial interpretations and assessments should be explored further.

There is greater Ksat & Kunsat particularly at the surface on the annual burn plots in the granites than basalts. These effects could be attributed to the loss of organic residues at the soil surface due to long-term fire treatments. As demonstrated by Fynn et al (2003), organic carbon was significantly reduced within the first 2 cm of the soil profile under repeated grassland dry annual and biennial winter fire treatments at Ukalinga in KwaZulu-Natal, similar results were described by Mills & Fey (2004) on the EBPs. More recently soil carbon was shown to be lower on dry annual burns in the Mopani basalt EBPs (Holdo et al., 2011) and the  N’wanetsi string following 30 years of fire treatment showed a quarter lower organic carbon content than on the annual, biennial and triennial burns (Jones et al., 1990). However the basalts show a smaller variation in Ksat & Kunsat on the annual treatments than the control plots which may result from the development of a relatively homogenous soil layer structure on the more frequently burnt plots. This is due to loss organic matter and downward illuviation of finer material. The basis for this theory arises from two aspects:

First, the influence and importance of organic matter content on soil sheer strength is further demonstrated by Ekwue (1990), who showed that soil shear strength increased as a result of grass derived organic matter content. Therefore the annually burnt basalt plots of the KNP have reduced soil strength, resulting from a loss of organic carbon due to frequent grassland vegetation fires at the site.  This will make the basalt soils on burnt areas both susceptible to erosion and have reduced soil moisture retention properties. The above results of deeper soil penetration per unit energy on the annual basalt plots described in this communication would support this hypothesis.

Second, DeBano (2000) discusses the role of fires in facilitating the development of a water repellent layer in the soil subsurface. The frequent annual burning on the basalt plots could lead to the formation of a water repellent layer below the surface rather than as a crust at the surface as suggested by Mills & Fey (2004). The small variation in Ksat at 5 cm on the basalt annual plots compared to the control is supportive of this theory, but warrants more detailed assessment, replication and analysis.

Results from this preliminarily assessment of the impact of long-term fire treatments on in-situ soil hydrology indicate that frequent hot fires lead to structural homogenisation of the soil surface on basalt soils  Interpretation of this dataset requires cognisance of other recent findings on the effects of fire frequency and season on the KNP landscape. The reduction in woody vegetation cover as a result of frequent burning (Smit et al., 2010) and increase in small tree dominance under frequent burning (Higgins, et al., 2007) are bound to have an effect on soil structure, as suggested by the scale dependent controls on biogeochemical processes resulting from tree canopy size (Holdo et al., 2011). Results will need to be discussed in this light. Whilst most interpretations and explanations have focused on the vegetation (both woody and grass) feedbacks on soil hydrological properties through a fire driven system, changes in herbivore utilisation and density  (e.g. Burns et al., in review) and resultant trampling and nutrient deposition as a result of fire treatments also needs to be considered.

This study indicates interesting geologically specific feedbacks between fire and soil hydrology. These need to be more thoroughly determined in order to quantify the impacts of soil crusting and water repellency resulting from fire on plant available water in the savanna landscape.

Acknowledgments

The authors acknowledge the contributions from the following people: Dr Pieter Le Roux (University of the Free State) for assisting with site selection based on soil diagnostics. Renson Thethe & Thomas Rikombe (SANParks) for protection whilst in the field. Johannes Hachmann (Vrije Universiteit, Amsterdam) provided additional assistance during the field campaign.

References

ANDERSEN, A.N., G.D. COOK & R.J. WILLIAMS. 2003. Fire in Tropical Savannas: the Kapalga Experiment. Springer Verlag: NewYork.

BIGGS, R., H.C. BIGGS, T.T. DUNNE, N. GOVENDER, A.L.F. POTGIETER. 2003. Experimental burn plot trial in the Kruger National Park: history, experimental design and suggestions for data analysis. Koedoe 46(1): 1-15.

BIJKER, H.J., P.D. SUMNER, K.I. MEIKLEJOHN & G.J. BREDENKAMP. 2001. Documenting the effects of veld burning on soil and vegetation characteristics in giant’s castle game reserve, KwaZulu-Natal, Drakensberg. South African Geographical Journal 83: 28-33.

BOND, W.J & J.E KEELEY. 2005. Fire as a global herbivore: the ecology and evolution of flammable ecosystems. Trends in Ecology and Evolution 20 (7): 387-394.

BROWN, J.A.H. 1972. Hydrologic effects  of  a  bushfire  in  a  catchment  in  south-eastern  New South  Wales. Journal of Hydrology 15: 77-96.

BURNS, C.E., A.D. ZINN, N. GOVENDER, G.M. BUIS & M.D. SMITH. in review 2011. The distribution of large herbivores in a fire-managed savanna grassland:  Assessing the role of bottom-up processes. Oikos.

DEBANO, L.F. 2000. The role of fire and soil heating on water repellency in wildland environments : a review. Journal of Hydrology 231: 195-206.

EIJKELKAMP AGRISEARCH EQUIPMENT. 2008. Operating Instructions: Geulph Permeameter, Giesberg, The Netherlands

http://pkd.eijkelkamp.com/Portals/2/Eijkelkamp/Files/Manuals/M1-0907e%20Guelph%20permea.pdf (last access: December 2011).

EIJKELKAMP AGRISEARCH EQUIPMENT. 2009. Operating Instructions: Pocket Penetrometer, Giesberg, The Netherlands

http://pkd.eijkelkamp.com/Portals/2/Eijkelkamp/Files/Manuals/M1-0603e%20Pocket%20penetromet.pdf (last access: December 2011).

EIJKELKAMP AGRISEARCH EQUIPMENT. 2011. Operating Instructions: Pocket Vane Tester, Giesberg, The Netherlands

http://pkd.eijkelkamp.com/Portals/2/Eijkelkamp/Files/Manuals/M1-1410e%20Pocket%20vane%20test.pdf (last access: December 2011).

EKWUE, E.I. 1990. Organic-matter effects on soil strength properties. Soil and Tillage Research 16(3): 289-297.

FYNN, R.W.S., R.J. HAYNES & T.G. O'CONNOR. 2003. Burning causes long-term changes in soil organic matter content of a South African grassland. Soil Biology and Biochemistry 35(5): 677-687.

GERTENBACH, W.P.D. 1983. Landscapes of the Kruger National Park. Koedoe 26:  9-121.

HERRICK, J.E. & T.L. JONES. 2002. A dynamic cone penetrometer for measuring soil penetration resistance. Soil Science Society of America Journal 66: 1320-1324.

HIGGINS, S.I., W.J. BOND & W.S.W. TROLLOPE. 2000. Fire, resprouting and variability: a recipe for grass-tree coexistence in savanna. Journal of Ecology 88: 213-229.

HIGGINS, S.I., W.J.  BOND, E.C. FEBRUARY, A. BRONN, D.I.W. EUSTON-BROWN, B. ENSLIN, N. GOVENDER, L. RADEMAN, S. O’REGAN, A.L.F. POTGIETER, S. SCHEITER, R. SOWRY, L. TROLLOPE & W.S.W. TROLLOPE. 2007. Effects of four decades of fire manipulation on woody vegetation structure in savanna. Ecology 88(5): 1119-1125.

HOLDO, R.M., M.C. MACK & S.G. ARNOLD. 2011. Tree canopies explain fire effects on soil nitrogen, phosphurus and carbon in a savanna ecosystem. Journal of Vegetation Science. DOI 10.1111/j.1654-1103.2011.01357.x.

JONES, C.L., N.L. SMITHERS, M.C. SCHOLES & R.J. SCHOLES. 1990. The effect of fire frequency on the organic components of a basaltic soil in the Kruger National Park. South African Journal of Plant Soil 7(4): 236-238.

KNAPP, A.K., J.M. BRIGGS, D.C. HARTNETT & S.L. COLLINS. 1998. Grassland Dynamics: Long-term Ecological Research in Tallgrass Prairie. Oxford University Press: NewYork.

LINDLEY, A.J., J.M. BOSCH & D.B. VAN WYK. 1988. Changes in water yield after fire in fynbos catchments. Water SA 14(1):  7-12.

LORENTZ,  S., S. THORNTON-DIBB, J.J. PRETORIUS & P.GOBA. 2003. Hydrological Systems Modelling Research Programme Hydrological  Processes,  Phase  II  Quantification  of  Hillslope,  Riparian  and  Wetland Processes,  Report  to  the Water  Research  Commission  on  the  Project  A  Field  Study  of  Two  and Three  Dimensional  Processes  Water Research  Commission,  Pretoria,  South  Africa  WRC  Report K5/1061 pp144

MILLS, A.J. & M.V. FEY. 2004. Frequent fires intensify soil crusting: physicochemical feedback in the pedoderm of long-term burn experiments in South Africa. Geoderma 121: 45-64.

SCHOLES, R.J. & B.H. WALKER. 1993. An African Savanna - Synthesis of the Nylsvley Study. Cambridge University Press, Cambridge.

SCHOLES, R.J. & D.O. HALL. 1996. The carbon budget of tropical savannas, woodlands and grasslands. Pg. 69-100. In: BREYMEYER,  A.I., HALL DO., MELILLO JM. AND AGREN GI. (eds.). Global Change: Effects on Coniferous Forests and Grasslands, SCOPE, Wiley, Chichester.

SCOTT, D.H. 1997. The Contrasting Effects of Wildfire and Clearfelling on the Hydrology of a Small Catchment. Hydrological Processes 11: 543-555.

SMIT, I.P.J., G.P. ASNER, N. GOVENDER, T. KENNEDY-BOWDOIN, D.E. KNAPP & J. JACOBSON. 2010. Effects of fire on woody vegetation structure in African Savanna. Ecological Applications 20(7): 1865-1875.

SOIL CLASSIFICATION WORKING GROUP. 1991. Soil classification: a taxonomic system for South Africa. Memoirs on the Agricultural Natural Resources of South Africa No. 15. SIRI, D.A.T.S., Pretoria.

TOWNSEND, S. & M. DOUGLAS. 2000. The effect of three fire regimes on stream water quality, water yield and export coefficients in a tropical savanna (northern Australia). Journal of Hydrology 229: 118-137.

STATEXT (2011) www.statext.com.

VAN DER SCHIJFF, H.P. 1958. Inleidende verslag oor veldbrandnavorsing in die Nasionale Krugerwildtuin. Koedoe 1: 60–93.

VENTER, F.J. & N. GOVENDER. in press 2011. A geomorphic & soil description of the long-term fire experiment in the Kruger National Park, South Africa. Koedoe

WALTER, H. 1971. Natural savannahs as a transition to the arid zone. Pg. 238 – 265. In: OLIVER & BOYD (eds.). Ecology of tropical and subtropical vegetation. Edinburgh

WEBBER, C.N. 1979. The effects of fire on soil-plant ecological relationships in the southern part of the Kruger National Park: a study in soil geography. MSc thesis, University of Pretoria, Pretoria.